## Slide 1: Traffic flow
Part 1: Constant Lambda
Joel Chavali
Vistas In Advanced Computing
August 11, 2017
Racing Theme

## Slide 2: Description
Model of Traffic Flow along a single lane.
Only the first vehicle varies
Following vehicle’s are dependent on the previous vehicles speed and a constant
Constant determined by user.
Race Strip

## Slide 3: Mathematics and equations
General Equation
What it means: Acceleration tied to Velocity
  Limited to only velocities
Discretized:
*Major Problem O(dt)
Legend of Symbols | 
 | Acceleration of the jth vehicle
 | Constant that user defines
 | Real Time Speed of Previous Car
(t) | Real Time Speed of Current Car
Legend of Symbols | 
 | Acceleration of the jth vehicle
 | Constant that user defines
 | Real Time Speed of Previous Car
 | Real Time Speed of Current Car
Math Clip Art
Scholarly by hand
Design of Car on Paper
This Photo by Unknown Author is licensed under CC BY-ND
This Photo by Unknown Author is licensed under CC BY-ND

## Slide 4: Runge-kutta 4th Order Pseudocode
First Step
Second Step
Third Step
Final Step
Picture of Runge-Kutta
Computer Code/Big Number Crunch
Computer Graphics Car or Unveiling

## Slide 5: Implementation
Problem about Displacement
  Order of Magnitude of Error
  Planetary Motion Example
Code
Mounting Tires, Installing Engine
Picture of Code,
Picture of Functions

## Slide 6: Implementation – Specifications
Maximum Time: Limit 37 s
Change in Time: 0.10 (for video purposes)
Max Acceleration: 7.276 m/s2 ( 23.87 ft/s2)
Max Velocity: 49.174 m/s ( 110 mph )
Initial Velocity: 30.0 m/s ( 67.1 mph )
Ind. Vehicle Length: 4.80 m ( 15.7 feet )
Lambda: 0.90
Mounting Tires, Installing Engine
Picture of Code,
Picture of Functions

## Slide 7: Scenario overviews
Vid of all three things goes here. Add labels as necessary
Tires Strip Down the left Side

## Slide 8: Steady state
Vid goes here
Open highway picture
Line of cars, high speed( race )
Tire Background
All vehicles remain at initial velocity for the entire interval.
Kind of boring
Program Specs:
Time: 30 s
dt: 0.1 s
Lambda: 0.90
Veh Length: 4.80 m
Init Sep Dist: 80.00 m
Init Vel: 30.00 m/s

## Slide 9: Acceleration
Vid goes here
NASCAR Just Start
Tires Down Side
Vehicles accelerate 30% from a steady state.
More Realistic, Everyday Driving
Small Increases and Decreases in speed due to road.
Program Specs:
Time: 30 s
dt: 0.1 s
Lambda: 0.90
Veh Length: 4.80 m
Init Sep Dist: 80.00 m
Init Vel: 30.00 m/s

## Slide 10: Deceleration
Vid goes here
NASCAR Just Start
Tires Down Side
Vehicles decelerate 30% from a steady state.
More Realistic, Everyday Driving
Small Increases and Decreases in speed due to road.
Program Specs:
Time: 30 s
dt: 0.1 s
Lambda: 0.90
Veh Length: 4.80 m
Init Sep Dist: 80.00 m
Init Vel: 30.00 m/s

## Slide 11: accelerating from Rest
Vid goes here
Drag Race
Truck Drag Race
Drag Race Christmas Tree
Tire Background
Lane of cars accelerate to 42 m/s from rest.
Real Life, Happens briefly at lights, Highway On Ramps
Program Specs:
0 -> 42 m/s
Time: 30 s
dt: 0.1 s
Lambda: 0.90
Veh Length: 4.80 m
Init Sep Dist: 80.00 m

## Slide 12: Decelerating to a stop
Vid goes here
Tire Down Side
Race Car Crash, Red Flag
Line of vehicles decelerates to rest at their maximum braking power.
Usually only in Emergency Stopping
Responding to Crashes
Pedestrian or Obstruction
Program Specs:
30 -> 0 m/s
Time: 30 s
dt: 0.1 s
Lambda: 0.90
Veh Length: 4.80 m
Init Sep Dist: 80.00 m

## Slide 13: Changing initial position (Broad)
Varying the Initial Separation Distance
  Optimize Traffic Loads on Roads
Model Specifications
  Decelerate to Stop
  Time: 30 s
  dt: 0.1s
  Lambda: 0.9
  Veh Length: 4.80 m
  Initial Velocity 30 m/s
Vid Goes Here
Cars Spread Out

## Slide 14: Changing initial position (fine)
Model Specifications
  Decelerate to Stop
  Time: 30 s
  dt: 0.1s
  Lambda: 0.9
  Veh Length: 4.80 m
  Initial Velocity 30 m/s
Min Sep Dist: 37 m
Practical Sep Dist: 50 m
Limitations
  Reaction Time
  Mechanical Delay
Vid Goes Here
Cars Bumper to Bumper

## Slide 15: Changing lambda
Increase Lambda
  Quicker Reactions
  Maintained Separation (Equation)
Limitations
  Maintained Separation
Model Specifications
  Decelerate to Stop
  Time: 30 s
  dt: 0.1s
  Headway: 80 m
  Veh Length: 4.80 m
  Initial Velocity 30 m/s
This Photo by Unknown Author is licensed under CC BY

## Slide 16: Comparing conventional vs optimized traffic
Optimization Increases Traffic Loads on Roads.
Vids Go Here (Formatting so 1 at a Time
Fine Tuning Spec for Race Car in Background?
Measurement Tools
This Photo by Unknown Author is licensed under CC BY-NC-ND
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 17: Comparing conventional vs optimized traffic
Acceleration and Deceleration: Smaller Headway yet
maintaining safety.
Vids Go Here (Formatting so 1 at a Time
Fine Tuning Spec for Race Car in Background?
Measurement Tools
Model Specifications: Time: 30 s, dt: 0.1s, Lambda: 2.3, Headway: 50 m, Initial Velocity 30 m/s

## Slide 18: Comparing conventional vs optimized traffic
Emergency Acceleration and Deceleration: Still
keeping passengers safe while adding more space for
larger roads capacity

## Slide 19: Applications Of Model
Humans too irregular
Automated Traffic is much more
  Precise
  Knowledgeable about neighbors
Used to find maximum load of a single lane highway
Maintain Safety Above All
Automated Car

## Slide 20: Multi – Create and Run future goals of model
Learned how to Create and Run Multiple Files at once w/ little user interaction
Model has capability to run with different vehicle specifications
  Lambda
  Initial Velocity
  Initial Separation Distance
  Vehicle Length
  Maximum Acceleration
  Maximum Velocity

## Slide 21: Sources
https://www.michigan.gov/documents/msp/BrakeTesting-MSP_VehicleEval08_Web_221473_7.pdf